## Slide 1: Requirements Engineering From System Goals to UML Models to Software Specifications
Axel Van Lamsweerde

## Slide 2: Chapter 6 Requirements Evolution

## Slide 3
start
Chap. 2:
Elicitation
Chap. 3:
Evaluation
alternative options
agreed
requirements
documented requirements
consolidated
requirements
Chap. 4:
Specification
Chap. 5:
Quality assurance
Chap.1: RE products and processes
Chap. 6: Evolution management

## Slide 4: Requirements evolution: outline
The time-space dimensions of evolution: revisions and variants
Change anticipation
Traceability management for evolution support
Change control: Change initiation/Change evaluation & prioritization/Change consolidation.
Runtime monitoring of requirements and assumptions for dynamic change.
Notes: 4

## Slide 5: The time-space dimensions of evolution: revisions & variants
Version: Every evolution cycle produces a new version of the RD. A new version may be a revision or a variant.
Revision: results from changes made to correct or improve the current version of a single product.
Variant: result from changes made to adapt, restrict or extend a master version.
Revisions result from evolution over time <=> Variants result from evolution across product lines.

## Slide 6: The time-space dimensions of evolution: Evolution types and causes
Changes in RD may be of different types, caused by different factors, resulting in different types of versions and operated at different phases of software lifecycle.
The linking of change causes, types, results and timing there is indicative of the complexity of the evolution process.

## Slide 7
The time-space dimensions of evolution: Evolution types and causes
Cause factor | Change Type | Version Type | Change time
Errors and flaws in the RD | Correction | Revision | RE, design, implementation, after deployment
Better customer understanding | Correction, extension | Revision | RE, (design), (implementation), after deployment
New functional features | Extension | Revision, Variant | (RE), (design), (implementation), after deployment
Environmental change: Alternative way of doing things | Adaptation | Variant | RE, (design), (implementation), after deployment
Environmental change: Organisational changes | Adaptation | Revision | (RE), (design), (implementation), after deployment

## Slide 8: Change anticipation
Anticipation: effective support of changes in system objective, conceptual structures, requirements, assumptions,… from the very beginning of the project.
Change anticipation: classifying a requirement/assumption as:
  Stable or Volatile from one system revision to the other.
  Common or distinct from one system variant to the other.
Associates levels of stability or commonality with statements.
  Ex. Figure 6.2 suggests a feature ranking for the Meeting Scheduling System.

## Slide 9
Change anticipation- heuristic rules
Regroup within features cohesive sets of statements that share the same stability or commonality level and address the same system objectives.
To help identify the most stable features, ask yourself what useful subset of features should be found in any contraction, extension or variant of the system
Intentional and conceptual aspects are more stable than operational and factual ones
Functional aspects related to the core objectives of the system are more stable than non-functional constraints for improvement of technology adaptation
Decision among multiple options deserve special scrutiny

## Slide 10: Traceability management for evolution support
Traceability management refers to the process of establishing, recording, exploiting and maintaining traceability links in a traceability graph.
Traceability management allows us to assess the impact of changes and to propagate actual changes for consistency maintenance within the RD and throughout the software lifecycle.
We may see it as “the art of documenting for evolution”

## Slide 11: Traceability management for evolution support: Traceability links
In a production chain, an item is traceable if we can fully figure out:
  Where the item comes from
  Why it comes from there
  Where it goes to.
Item traceability relies on the existence of links between items that we can follow backwards (towards source items), and forwards (towards target items).
In RE, traceability concerns a diversity items:
  RD items such as objectives, concept definitions, functional and non-functional requirements and assumptions.
  Downward software lifecycle items such as design specifications, architectural decisions, test data, user manuals, source code, software documentation, project reports.

## Slide 12: Traceability management for evolution support: Traceability links (cont.)
Forward & Backward traceability
Horizontal traceability
  An RD item may rely on other same level items (req relies on assumptions). Such traceability is called horizontal traceability.
Vertical traceability
  An RD item may originate from upward items or give rise to lower-level RD items/downward software lifecycle items. Such traceability is called vertical traceability.

## Slide 13: Traceability management for evolution support: Traceability links (cont.)
Dependency link: There is a dependency link between a target item B and a source item A if changing A require changing B.

## Slide 14: Traceability management for evolution support: Traceability links (cont.)
Variant link: There is a variant link between a target item B and a source item A if B has all the features of A while having its own distinguishing features.
Revision link: There is a revision link between a target item B and a source item A if B overrides certain features of A, adds new ones and/or removes others, while keeping all remaining features.
Use link: There is a use link between a target item B and a source item A if changing A makes B become incomplete, inadequate, inconsistent or ambiguous.
Derivation link: There is a derivation link between a target item B and a source item A if B is build from A under the constraint that A must be met.

## Slide 15: Traceability management for evolution support: Traceability management process
Traceability management refers to the process of establishing, exploiting and maintaining traceability links. This process provides multiple benefits for an extra cost to pay.
Define Policy: Project-specific traceability policy should be defined as an initial step of the process towards some optimal cost-benefit trade-off.
Establish links: the link granularity, link semantic richness, link accuracy , and link overhead

## Slide 16: Traceability management for evolution support: Traceability management techniques
Cross referencing
Traceability matrices
Feature diagrams
Traceability databases
Traceability model databases
Specification-based traceability management
Traceability link generators
Consistency checkers

## Slide 17: Change control: Change initiation
The team in charge of project maintains a wishlist of possible changes (identified by insiders or collected from outsiders).
At certain time intervals (causal factors, degree of emergency, policy), the team consolidates the wishlist into a change request.
For each proposed change, following information provided:
  Its description
  Its context
  The rationale for this change.
  The system stakeholder who asked for it.
  A first estimation of the change impact
  A first estimation the cost & resources required.
The change request is submitted to review-board.

## Slide 18: Change control: Change evaluation & prioritization
The review board is responsible to assess the merits, feasibility and cost of the proposed changes in the change request.
The review board needs to do the following:
  Understand the context of the requested change.
  Assess the benefits of proposed change.
  Assess their impact n other items along traceability links.
  Detect potential conflicts among the proposed changes.
  Assess the risk of change against the risk of non-change.
  Estimate the cost and feasibility of the changes.
  Prioritize the accepted changes.
In general, some proposed changes are approved, others are rejected and others are deferred.

## Slide 19: Change control: Change initiation
Handling all approved changes to produce a new system version.
  Forward propagation of all approved changes through the RD along horizontal links of traceability graph.
  Baselining of the new version of the RD for sharing among project members until the next version is baselined.
  Forward propagation of all RD changes downward to software lifecycle items along vertical links of traceability graph.
  Updating of the traceability graph.

## Slide 20: Runtime monitoring of requirements and assumptions for dynamic change
Requirements monitoring is a recent paradigm for dynamic change at system runtime.
  Monitors are built for requirements/assumptions that are felt to be critical or too volatile.
  Monitor run concurrently with the system-to-be to detect event consequences that violate the monitored assertions.
  At development time, for each monitored statement, some alter course of actions are designed, if we want to shift to it at system runtime.
  Monitor may report such violations to a rule-based compensator for system reconfiguration.
  Assertion monitors can be automatically generated if the req/assumptions to monitor are specified formally.

## Slide 21: Requirements evolution: summary
The time-space dimensions of evolution: revisions and variants
Change anticipation
Traceability management for evolution support
Change control: Change initiation/Change evaluation & prioritization/Change consolidation.
Runtime monitoring of requirements and assumptions for dynamic change.